## Slide 1
Results
Conclusion
ROC-DRAM: Low Latency and Low Power DRAM
using Rows with Opposite Charging
Jaeyoon Lee, Daero Kim, and Jungrae Kim
Introduction
This paper proposes a novel DRAM architecture, called Rows with Opposite Charging DRAM (ROC-DRAM), to provide efficient and flexible trade-offs among capacity, performance, and energy consumption to exploit under-utilized memory capacity in data centers. ROC-DRAM stores a bit of information in two cells in paired rows with opposite charge levels to trade capacity for performance and low power. And ROC-DRAM supports dynamic mode switching between max-capacity, low-latency, and low-power modes based on memory capacity utilization and application requirements. The proposed architecture demonstrates significant improvements in performance, energy efficiency, and refresh overheads, making it a promising solution for data centers with under-utilized memory capacity.
Problem
DESIGN AUTOMATION CONFERENCE’23
DRAM access latency plays a critical role in modern computers. Prior works suggested latency optimizations, yet cost-sensitive DRAM vendors are reluctant to sacrifice their area efficiency. This paper proposes a novel DRAM architecture that can dynamically trade DRAM capacity for low latency and low power with minimal costs. Rows with Opposite Charging DRAM (ROC-DRAM) can exploit under-utilized capacity to improve latency and power consumption. It stores data in two rows with opposite charge levels and feeds them to a bitline sense-amplifier. The larger gap from complementary cells allows faster sensing and longer retention time. Moreover, ROC-DRAM allows dynamic switching between max-capacity/low-latency/low-power modes to maximize savings.
Abstract
In the open-bitline structure, a BLSA receives bitlines (bitline and /bitline) from two vertically adjacent mats. Only one mat can be activated at a time, while the other mat is inactivated. The bitlines of the inactivated mat (/bitline) are precharged to VDD/2 and serve as the reference voltage for the shared BLSA to sense the activated bitline (bitline).
DRAM access latency is crucial in modern computers, but cost-sensitive DRAM vendors hesitate to optimize latency at the expense of area efficiency.
Goal
Improve access latency and refresh overheads in data centers with under-utilized memory capacity.
Key Idea
Leverages complementary cells to enable faster sensing operations and extended retention times with minimal modifications to the DRAM internal structure.
Conventional Structure
Proposed Method
ROC-DRAM
Supports low-latency and low-power modes (right figure), in addition to the default max-capacity mode (left figure).
Accelerated sensing key DRAM timing parameters (tRCD, tRAS, tWR, and tRFC). Rapid sensing is achieved as the discharged cell maintains a level close to GND, quickly pulling down the /bitline.
Allows for an increase in tREF. Referring to the /bitline written with GND creates resistance to cell charge loss. Allowing the charged cell to go far below VDD/2, as long as there is a sensible voltage difference between the original and complementary bitlines.
Figure compares IPC / Energy of the baseline open-bitline architecture and other modes of ROC-DRAM with ET. Overall, the LL mode can speed up single-core execution by 6.9% using 23 SPEC CPU 2006 benchmarks. Also, LL mode reduces DRAM energy consumption by 9.0% on average.
Low-
Latency
(LL)
Low-
Power
(LP)