## Slide 1: UVMMU: Hardware-Offloaded Page Migration for Heterogeneous Computing
Jihun Park, Donghun Jeong, and Jungrae Kim

## Slide 2
Introduction
GPU driver raises SW interrupt (Page Fault).
CPU handles page faults to prepare page migration.
Page is migrated through PCIe.
time
Page Fault
Page Fault Handling
Computation
GPU
CPU
Page migration
PCIe
45us
Impact of Page Fault
Zero page fault latency leads up to 2.74x speedup.
But, Practical lower bound of page fault latency is 20us.
Need low-cost HW solution!
Fault-based Page Migration Process

## Slide 3
UVMMU
UVMMU replaces GMMU to manage fast page migration preparation.
Provide destination/source frame addresses required for page migration.
Hardware details
DCQ stores destination frame-group candidates entry for page migration.
Available Frame Manager find free frame-groups to fill DCQ with.
In over-subscription, fill DCQ with random frame-group.
Overview

## Slide 4
Results
59.3% speedup over fault-based solution.
Large page fault handling delay (45us) is eliminated.
With Over-subscription
2.40x speedup in 150% over-subscription.
Page eviction increases costly page faults in fault-based solution.
Without Over-subscription
UVMMU reduces page migration overhead!

## Slide 5: Thank You

## Slide 6
Background
Heterogeneous Computing System
Heterogeneous System
CPU
GPU
CPU
Memory
GPU
Memory
PCIe
Need user-responsible data copy
Data size is limited by GPU memory capacity
Need data partitioning tasks

## Slide 7
Programmer’s View
CPU
GPU
CPU
Memory
GPU
Memory
PCIe
Shared Address Space
Page Migration
Background
Unified Memory System
Shared virtual address space among processors
On-demand page migration during kernel execution
Enable memory over-subscription
High programmability

## Slide 8
Background
Fault-based Page Migration
GPU driver raises SW interrupt (Page Fault).
CPU handles page faults to prepare page migration.
Page is migrated through PCIe.
time
Page Fault
Page Fault Handling
Computation
GPU
CPU
Page migration
PCIe
Fault-based Page Migration Process
45us

## Slide 9
Motivation
Impact of Page Fault Latency
Zero page fault latency leads up to 2.74x speedup.
But, Practical lower bound of page fault latency is 20us.
Need low-cost HW solution!

## Slide 10
UVMMU
Overview
Goal: Offload page migration entirely to the HW
UVMMU replaces GMMU
  Provide destination/source frame addresses required for page migration
  Search and prepare destination frame address in background
  Source frame address is stored in GPU page table

## Slide 11
UVMMU
Data Structure
Inverted Page-group Table (IPgT)
  Map of physical address to virtual address
  Identify free frame-groups by ‘free’ flag
Frame-region Available Bitmap (FrAB)
  Help faster free frame-group search
  Identify free frame-group’s existence in 2MB frame-region

## Slide 12
UVMMU
Hardware Details
DCQ
  Store destination frame-group candidates
  Entry is used for page migration
Available Frame Manager
  Search FrAB and IPgT to find free frame-group
  Fill DCQ with free frame-group
  In over-subscription, fill DCQ with random frame-group

## Slide 13
Evaluation
Methodology
NVIDIA GTX 1080 Ti Configuration | 
Core | 1481MHz, 28 SMs, 64 warps/SM
Cache Line | 128B Line with 4 sectors(32B)
L1 Cache | 48KB, 6 Way Associative
L2 Cache | 3MB, 16 Way Associative
L1 TLB | 128 entries Fully Associative
Memory | 11GB 484GB/s GDDR5X
Page Table Walker | 64 walkers
PCIe | PCIe 3.0 x16(16GB/s BW, 1us RTT)
Migration Handling Latency | 10 cycle (UVMMU), 45us (Baseline)
Simulator: UVMSmart(Extended GPGPU-sim)
  Add UM implementation
  Replace GMMU with UVMMU
  Add PCIe modeling

## Slide 14
Evaluation
Execution Time
Without Over-subscription
  59.3% speedup over fault-based solution.
  Large page fault handling delay (45us) is eliminated.

## Slide 15
Evaluation
Execution Time
With Over-subscription
  Result shows even larger performance gap.
  2.21x and 2.40x speedup in 125% and 150% over-subscription.
  Page eviction increases costly page faults in fault-based solution.

## Slide 16
Evaluation
Sensitivity Studies
Eviction Policy
  UVMMU utilizes Linear-Random policy for simple HW implementation.
  Competitive performance compared to other policies.
  UVMMU is insensitive to eviction policy due to low migration cost.

## Slide 17
Evaluation
Sensitivity Studies
Over-subscription Ratio
  UVMMU shows linear increase of execution time.
  Fault-based solution shows rapid growth (e.g., 2.27x for 150%).
  UVMMU exploits memory over-subscription with fewer overheads.

## Slide 18
Evaluation
Hardware overhead
Additional Area overhead of UVMMU
  5800 (0.0012% of GTX 1080 Ti die)
Additional Power Consumption
  65 mW (0.026% of GTX 1080 Ti TDP)
Tools Used
  Verilog RTL Design (Samsung 8nm process)
  CACTI (ITRS 22nm process)

## Slide 19
Conclusion
time
Page Fault
Page Fault Handling
Computation
GPU
CPU
Page migration
PCIe
time
H/W
Prep.
Computation
GPU
CPU
Page migration
PCIe
Fault-based Page Migration
UVMMU
UVMMU reduces page migration overhead!